## Slide 1: Fermentation Data Analysis (and other time course experiments)
Steve Van Dien
Nov. 29, 2018

## Slide 2: Agenda
Overview
Step-by-step demonstration of calculations, with example
Conceptual example – fatty acids in yeast
Hands on example using raw data spreadsheets – serine in E. coli

## Slide 3: Fermentation Overview
Benefits of Fermentation
  Tuning and control of aeration
  pH control
  Substrate feeding
  Off-gas analysis
  Facilitates time-course sampling
Objectives of Fermentation Experiments
  Evaluation of milestone strains at process conditions
  New strain evaluation
  Condition optimization- aeration, media, pH, temp
  Detailed strain evaluation
  Diagnostic experiments
  Scale-up
High cell density and product titer
Accurate calculation of rates

## Slide 4: Calculation of Rates in Fermentation
Calculation of specific rates (mmol/gDCW-hr) over each time interval facilitates understanding of cell physiology
Independent of volume changes
Inputs for constraint-based modeling
How to get there
  Determine all system inputs, outputs, and accumulation
  Convert to cumulative mmoles of each produced or consumed
  Evaluate carbon balance
  Calculate average specific rate over any time interval
  Calculate specific rates at each time point (various methods)

## Slide 5: Calculation of Liquid Volume
Accurate liquid volume needed to convert concentrations to amounts
Initial volume
Total amount of each substrate fed
Volume of base (or acid) fed
Volume of samples taken
Does not account for
  Loss of water vapor or volatile liquids in off-gas
  Changes in broth density
  Water produced or consumed during metabolism

## Slide 6: Products and Byproducts Formed
At any given time (t), total product formed is the amount in the tank at time t plus all removed by sampling
Product of Interest
Amount in tank = conc x volume at t
Amount in sample = conc x vol
at each time point
Analogous equations for all soluble byproducts

## Slide 7: Carbon Source Consumed
Initial CS:
Continuous feed
Bolus feed
(Often zero)
Residual:
F = volumetric flowrate
Can also measure weight if feed on scale

## Slide 8: Example: Biotransformation
Cells are grown on glucose, then pathway is induced to convert substrate to product
Aerobic process – oxidative biotransformation

## Slide 9: Example: Biotransformation

## Slide 10: Consumption and Production

## Slide 11: Product and Byproduct Yields
Once the product formed and carbon source consumed are determined, yields can be calculated
Calculate amount of CS consumed in seed based on volume of inoculum, not entire seed tank
In not measured, can estimate:

## Slide 12: Off-gas Calculations
Oxygen uptake rate (OUR) and CO2 evolution rate (CER) are calculated from off-gas analysis
Units are mmol/hr
O2 and CO2 are the mol% of each in the off-gas
Fair is the air flowrate at a given time, L/min
P is the pressure (atm), T is temperature in K
X is the inlet %O2, equal to 21% for pure air
Cumulative amount of O2 consumed or CO2 produced is calculated by integrating up to time t

## Slide 13: Off-gas Analysis

## Slide 14: Other Calculations
Biomass:
Specific OUR:
Growth Rate:
Substrate Uptake Rate:
Volumetric OUR:

## Slide 15: Off-gas Analysis
Respiratory quotient: RQ = CER/OUR
RQ > 1 may indicate oxygen limitation

## Slide 16: Total mmoles produced or consumed

## Slide 17: Interval Uptake and Production Rates
Product (or any liquid-phase byproduct):
Analogous equations for substrate uptake
Can also determine specific rates – divide by average biomass
Can also calculate interval yields at each time point

## Slide 18: Interval Uptake and Production Rates
Calculated rates are just an approximation of derivative of cumulative mmol plot – usually based on sparse sampling
Specific rates have additional uncertainty of biomass measurement
Various ways to calculate, potentially giving different results if sampling is infrequent
  Use t and t-1
  Use t+1 and t-1
  Use average biomass or estimate based on growth rate?
  Curve fitting followed by analytical differentiation may be the most accurate
Warning!

## Slide 19: Rates Calculated for Example

## Slide 20: Carbon Balance
For E. coli, #C in OD determined to be about 17
Carbon balance is useful to determine the quality of the measurements, and used to track down missing products.

## Slide 21: Carbon Balance
Carbon in lower than carbon out because uptake from rich media is not measured

## Slide 22: Degree of Reduction Balance
Useful for QC, especially for oxygen measurement
Generally not as accurate as carbon balance
For any compound CaHbOcNd SePf , DOR = 4a + b –2c – 3d + 6e + 5f

## Slide 23: Example – Fatty Acid Production in Yeast
Removed PDC genes to prevent ethanol production
Added citrate lyase to generate cytosolic acetyl-CoA
Inserted heterologous pathway for free fatty acid synthesis

## Slide 24: Example – Fatty Acid Production in Yeast
Convert all data to cumulative mmoles produced

## Slide 25: Example – Fatty Acid Production in Yeast
Calculate rates over each time interval